Linear Profile Monitoring for an AR(1) Process

Yi-Hua Tina Wang*, Wan-Hsuan Huang

Department of Statistics, Tamkang University, Taiwan

Abstract

In most control chart applications, the quality of a process can be adequately represented by the distribution of some important quality characteristics. However, in some applications the quality of a process or product is better characterized and summarized by a functional relationship between a response variable and one or more explanatory variables. A collection of this kind of data points is called a profile. Profile monitoring is used to understand and to check the stability of this relationship or curve over time. The independence assumption for the error term is commonly used in the existing simple linear profile models. In this study, we focus on a simple linear profile model but there is a first order autocorrelation between profiles. We propose different monitoring statistics and derive their control limits for phase II monitoring. The proposed methods are shown to have good performance in the simulation study based on the ARL criterion.

Keywords: Linear profile monitoring, autocorrelations, EWMA control charts, average run length.