道路評審儀數據處理與路面結構指標之結合運用

This study is to propose a new Deflection Index estimation based ondynamic stress analysis and pavement conditions of domestic highway tomeet the needs of steady-state deflection test (Road Rater) as well asimpact deflection test (FWD). The estimation can offer highwaymaintainer agencies convenient procedures in determining the pavementstructural capacity. Result shows that the new Deflection Index Methodcan yield compatible results with those founded empirically. Theefficiency of the method is indicated in supervising the pavementbefore and after the overlay. In addition, the pavement evaluation hasconsistency with the out come of dynamic backcalculation analysis.