A Position Sensorless Phase Commutation Control to Minimize Torque Ripple of Hybrid Step Motor

This paper presents a position sensorless phase commutation control scheme to minimize torque ripple for motor step motor. An observer based on the measurement of motor back emf and phase current is utilized to estimate the motor electrical angle for phase commutation. The proposed control scheme uses the same hardware as the open loop step motor controller except for the addition of voltage and current sensors.