Fair Bandwidth Allocation Fuzzy Controller for the Ieee 802.11 Multiple Data Rate Infrastructure Networks

This paper will discuss the issues of supporting multiple data rates (1/2/5.5/11Mbps) over an infrastructure wireless network. With the characteristic of modulation schemes, the data rate is inversely proportional with the transmission distance. A moving mobile station needs dynamically adjust its modulation scheme to achieve maximum network throughput and to keep the connection alive. In this paper, we will introduce a simple broadcasting approach to inform mobile stations the location information. Moreover, a hybrid handshaking protocol is also designed to help maintaining high channel utilization. Finally, the fairness problem of multi-rate wireless network is also being discussed and solved by using the proposed fuzzy controller.