A Power Saving Sleep Scheduling based on Transmission Power Control for Wireless Sensor Networks

Ying-Hong Wang, Ya-Lan Wu

Department of Computer Science and Information Engineering,

Tamkang University Tamsui, Taipei, Taiwan, R.O.C.

Abstract- The relate technologies of Wireless Sensor Networks (WSNs) have become an essential research in the future. The sensor nodes of WSNs can only use limited energy like battery. When the energy has been exhausted, WSNs cannot work anymore. In order to extend the lifetime of WSNs, the management of the sensors’ energy is an important issue. The Sleep Schedule addressed on �A Power Control Mechanism based on Sleep Scheduling for Wireless Sensor Networks� cannot guarantee that neighbor node has ability to do transmission. Use the improved algorithm and the original algorithm to do simulation comparison. The improved algorithm which is better than the network without sleep scheduling algorithm can complete 40 rounds and has no data loss. As a result, the improved algorithm proposed in this thesis can effectively resolve the data loss problem of the original algorithm.

Keywords-Wireless Sensor Networks, Lifetime, Transmission Power Control, Sleep Scheduling

1.	Introduction

Recent advances in micro-electro-mechanical systems (MEMS) technology, wireless communications and digital electronics [1] have enabled the hardware of the embedded system that is small in size and can apply to the routers or the firewall in wireless network. Due to the limitation of the environment, charging or replacing power is impossible. Therefore, the power consumption speed influences the lifetime of the wireless sensor networks. How to extend the lifetime of the wireless sensor networks has become an important subject in the research of the wireless sensor networks.

The sensor node is made up of four basic components: a sensing unit, a processing unit, a transceiver unit and a power unit. Sensing unit is responsible for detecting the physical information like the light source, the hot source and the sound source. The analog signals produced by the sensors based on the observed phenomenon are converted to digital signals by the ADC, and then fed into the processing unit. The processing unit is responsible for processing the information which sent by the sensing unit. Then, the information would be sent back to the base station by the transceiver unit. Power unit is responsible for the power of the sensor node. The power consumption of the transceiver unit is the biggest in all of the units.

At present, there are the following methods in the research direction about power saving: 1. Sleep Scheduling [2, 3, 4]: Let the idle sensor nodes go asleep to conserve the energy. 2. Adjust the sensing range. 3. Send information to the base station through the effective route. 4. Decrease Overhead.

The concept of sleep scheduling is to let the state of the sensor nodes to be sleep mode and active mode. Two factors must be considered when designing sleep scheduling: 1. Extend the lifetime of the network, 2. Avoid the data loss. The sleep scheduling addressed in �A Power Control Mechanism based on Sleep Scheduling for Wireless Sensor Networks� [5] cannot guarantee that there are sensor nodes awake to do data transmission and it would be result in the data loss. The improved sleep scheduling proposed by this thesis is to resolve the data loss problem.

2.	Related Work

There are four major sources of the power consumption in WSNs [6]. 1. Collision: when packets collide, energy is wasted because the packets must be retransmitted. 2. Sparse: when sensor nodes are deployed sparsely in the sensing range, packet delivery range increasing compared to crowded nodes and the power consumption is high. 3. Overhead: all the neighbors of the transmitting node can potentially overhear a transmission between nodes, thus all of these nodes consume more power despite the packets not being directed to them. 4. Idle: A sensor node has transmission, receiving and idle state. In the idle state, nodes must listen to the channel to receive possible traffic and the power consumption is more than the node in sleep state. Nodes typically have several power levels corresponding to the following states: transmission, receiving, idle and sleeping. Usually, the power required for idle listening is about the same as the power for receiving [7].

In 2003, J. Chen [10] et al. proposed an algorithm which using different transmission methods for different nodes to conserve energy. In 2005, EI-Osery [12] et al. use the additional energy information from the receiving packets to figure out the optimum transmission power for sending packets to the source and create a table. If information needs to transmit later, it would follow this table to determine the transmission power. Kawadia and kumar [11] introduce some transmission power control protocols; one of them is CLUSTERPOW protocol, in which the concept is creating routing table by different kinds of transmission power. Floreen [13] et al. has done the transmission power control research for multicast.

For the subject of power saving in WSNs, sleep schedule is a major research direction. Wei et al. [3] proposed a Sensor Mac protocol which is a fixed sleep scheduling algorithm to avoid overhead and collision, and reduce the idle time to conserve energy at the same time. Brabara Hohlt, Lance Doherty and Eric Brewer [8] proposed a flexible power scheduling, a distributed power management protocol for sensor networks that reduces radio power consumption. It schedules transmitting and receiving time slots in each node’s power schedule and sleeping during idle periods. Mihail L. Sichitiu [9] proposed a Cross-Layer Scheduling Protocol to generate schedule table for transmitting, receiving and sleeping. The sleep scheduling addressed in �A Power Control Mechanism based on Sleep Scheduling for Wireless Sensor Networks� [5] uses the concept of duty cycle to figure out the active time and sleeping time dynamically, but it cannot guarantee that there are sensor nodes awake to do data transmission and it would be result in the data loss. The improved sleep scheduling proposed by this thesis is to resolve the data loss problem.

3.	Sleep Scheduling Algorithm based on Transmission Power Control

3-1	Transmission Power Control

In WSNs, if the energy of the battery is exhausted, the lifetime of the network would be suspended. Sensor node’s data transmission performing is the behavior which consumes the most energy. Therefore, to control the transmission power of the sensor node could reduce the nonessential power consumption.

For WSNs, an effective TPC may manage the massive sensor nodes in the wireless sensor network effectively to share wireless channel under the smallest disturbance with each other and achieve high quality of service (QoS), moreover it may reduce the power consumption of each sensor node in order and extend the lifetime of the entire wireless sensor network.

A kind of TPC applied in wireless sensor networks as shown in figure 1. This mechanism may reduce the power consumption when sensor nodes do data transmission and receiving. The operation of this TPC is for specific sensor node to seek neighbor nodes in different transmission power level. For node A, when transmission power level is set to 1, it can find 2 neighbor nodes. And when transmission power level is set to 2, it can find 7 neighbor nodes. And when transmission power level is set to 3, it can find 16 neighbor nodes. The higher transmission power level is set, the more neighbor nodes are found. But the higher transmission power level is set, the more energy of sensor node would be consumed. So need to adjust the transmission following the target node, in which transmission power level eliminates the unnecessary power consumption.

Figure 1. Transmission Power Control

3-2	Sleep Scheduling Algorithm based on Transmission Power Control

In the research about power consumption, the TPC is a common research method. TPC can be reached by saving some usable information like the transmission power of the different neighbor nodes, transmission distance and packets loss rate. �A Power Control Mechanism based on Sleep Scheduling for Wireless Sensor Networks� [5] proposed by Chin-Yung Yu in 2009 which is combined with TPC and Sleep Scheduling Algorithm to reduce the power consumption. But the Sleep Scheduling Algorithm cannot guarantee that neighbor node has ability to do transmission, because the node may be in asleep and it might be result in data loss. In this session, the concept of the transmission power level would be joined to the original sleep scheduling algorithm to resolve the problem of no neighbor node to do data transmission and reduce packets loss rate effectively.

When wireless sensor network initials, the tables would be created firstly and do the operation to figure out Ta and Ts for each node. If the node is in transmission state, Ta would be adjusted to guarantee the transmission to be accomplished. And if else, after the node wakes up, Ta and Ts would be figured out until the remnant energy is smaller than the transmission energy threshold and never do data transmission.

3-2-1	Create Tables

When create tables, Base Station would broadcast �Rest� packets to all sensor nodes in wireless sensor network. When all sensor nodes in wireless sensor network receive �Rest� packets, they would update the local information like Table 1 based on the �Rest� packet. Then each node would broadcast �RREQ� packet to those neighbor nodes in the maximum transmission distance (Txmax) such as the Txmax is 30m. Then the node would wait for the Wait Time and the neighbor nodes to reply �RREP� packet. Set the Wait Time is to let the neighbor nodes reply �RREP� packet opportunely. The information which are replied by neighbor nodes can be saved in the Neighbor Information Table for each node as shown in Table 2. Figure 2 is the initialization flow for creating tables.

Figure 2. Table initialization flow

��	Information Packets

There are three tables defined in this research. The first is Owner Information Table as shown in Table 1. The second is Neighbor Information Table as shown in Table 2. The third is Mica2 Power Table as shown in Table 3. The following step is detail description of each table:

1.)	Owner Information Table (OIT) has 15 fields:

1.	NodeID : serial number of each node

2.	X-axis : X axis

3.	Y-axis : Y axis

4.	Energy : Initial energy

5.	Remaining Energy : residue energy

6.	Rec. Energy : energy expended in receiving a packet

7.	Sleep Energy : energy expended when a node enters sleep mode

8.	Thold. Energy : transmit threshold energy

9.	Duty Cycle : the time period

10.	Active Time : the time when the node is put into active mode

11.	Sleeping time : the time when the node is put into sleep mode

12.	Status : the node’s current status

1: transmit; 2: receive; 3: act; 4: sleep; 5: die;

6: event node; 0: Base Station

13.	Layer : the layer is used to indicate the distance between the node and the base station for example the node is closest to the base station is layer 1. The layer range is from 1 to 20.

14.	PacketID : the id of the event node

15.	Wait Count : At the end of each round, when the node is in the idle state, the wait count is increased by one. When a count of three is reached, the count is reset to zero and the sleeping time of the node is extended by this amount at the next round. This prevents the node from being idle too long and conserves energy.

16.

Table 1. Owner Information Table (OIT)

2.)	Neighbor Information Table (NIT) has 9 fields:

1.	NodeID : the serial number of each node.

2.	Power Level : the power required to transmit a message to a neighbor node.

3.	NeighborID : the serial number of the neighbor node.

4.	Dis. NeighorID : the distance to a neighbor node.

5.	Layer : the distance between a neighbor node and the base station.

6.	RSSI : is a measurement of the power present in a received a radio signal.

7.	Active Time NeighborID : the time when a neighbor node is put into active mode.

8.	Sleeping time NeighborID : the time when a neighbor node is put into sleep mode.

9.	Receive Time : the time when receiving the update value of Active Time NeighborID and Sleeping time NeighborID. This value 0 means that the value of Active Time NeighborID and Sleeping time NeighborID has not been updated.

Table 2. Neighbor Information Table (NIT)

3.)	Mica2 Power Table (MPT) has 3 fields:

1.	Power Level : the power level of a mica2 device ranges from -20 to 5.

2.	Consumption : The energy consumed to transmit using each power level.

3.	Range : The range when transmitting at the current power level.

4.

Table 3. Mica2 Power Table (MPT)

Figure 3 shows the relationships between a mica2 device’s power level, energy consumption and ragne.

Figure 3. Mica2 device’s power level, energy consumption and range

3-2-2	Sleep Scheduling Algorithm

This sleep scheduling algorithm includes 6 steps. 1-4 steps use the Duty Cycle concept to adjust active time and sleeping time, 5-6 steps use the Transmission Power Level concept to filter the neighbor nodes in the same power level, let one node awake at least to perform data transmission. Before entering the first step, the node must renew the NIT firstly and confirm the information in NIT has been renewed. If the material has not been renewed, set its active time to 0 and sleeping time to duty cycle, then start sleep scheduling algorithm. At the first step, the node verifies that its residual energy is greater than the threshold energy so as to ensure that there is sufficient energy for the next transmission. If there is no sufficient energy, set the sleeping time of the node to the maximum and start sleeping state. If there is sufficient energy, enter the next stage. At the second step, it determines whether it is in a transmission state currently. If it is, the active time of the node is set to the maximum to allow the node complete its current transmission. If it is not, enter the next stage. At the third step, it determines its wait count is bigger than or equivalent to 3. If the wait count is bigger than 3, set an interrupt point time (Tirq) to interrupt the active time of the node and extend the sleeping time of the node. If the wait count is smaller than 3, enter the next stage. At the forth step, it checks whether the node residual energy/initial energy ratio is above 50%. If it is above 50%, then the active/sleeping times are randomly set, else the current active time is compared with a randomly generated active time and the smaller of the two times is selected as the next active time. At the fifth step, use the active time and sleeping time which is generated at step 3 to compare with all neighbor nodes in the same transmission power level. If all nodes sleep at the same time, extend the active time of the node until at least one neighbor node awake. The sixth stage is like the fifth stage. Finally, broadcast the Ta and Ts and set the value of receive time in NIT to 0. Upon executing the above stages, this algorithm can dynamically adjust a sleep schedule for sensor nodes to reduce unnecessary power consumption and it also can guarantee that the nodes are awake to do the transmission for reduce data loss rate. Every step is further illustrated in Figure 4.

Figure 4. Sleep Scheduling Algorithm base on TPC

Figure 5 is an example which needs to adjust active time and sleeping time to prevent all nodes at the same transmission power level sleeping together. Node A, B, C and D are in the same transmission power level. Node B, C and D are the neighbor nodes of node A. After node A is awake, performing Sleep Scheduling algorithm to figure out active time and sleeping time. The value need to compare with the active time and sleeping time of node B, C and D. As shown in Figure 5, S’B, S’C and S’D are all bigger than Ta. It means that at some time node A, B, C and D are all in sleeping. To prevent all sensor nodes at the same transmission power level sleeping together, extend the active time of node A until at least one node is awake. The node B which is awaken fastest, so use node B to adjust the active time and sleeping time of node A.

Ta of node A = Ta + (S’B - Ta)

Ts of node A = Ts – (S’B - Ta)

Figure 5. Case 1 need to adjust Ta and Ts

Figure 6 is an example which does not need to adjust active time and sleeping time. After node A is awake, performing Sleep Scheduling algorithm to figure out active time and sleeping time. The value need to compare with the active time and sleeping time of node B, C and D. As shown in Figure 6, S’B is smaller than Ta. This means that before node A go sleeping, node B has awakened. So the active time and sleeping time of node A does not need to be adjusted.

Figure 6. Case 2 not need to adjust Ta and Ts

��	Update NIT

To know that if all sensor nodes which in the same transmission power level are sleeping together, sensor node must renew the active time and sleeping time in NIT. Two update methods define in this research: 1. Update from neighbor node; 2. Update from local node. The following is the detail description for these two methods.

After sensor nodes execute sleep scheduling algorithm to figure out active time and sleeping time, they would broadcast their Ta and Ts automatically. After receiving the broadcast message, the neighbor nodes would renew their NIT. This update procedure is called Update from neighbor node. But when the neighbor nodes are in sleep, this update procedure cannot be executed properly. So it needs to do update from local node.

After sensor nodes awaken, they need to execute update from local node first. The node would send �RREQ� packet to those neighbor nodes which receive time is 0 in NIT. Then the node would wait for the Wait Time for the neighbor nodes to reply �RREP� packet. The response information would be saved in NIT. Figure 7 is the flow of update NIT from local node.

Figure 7. Update NIT table

Figure 8 is an example to update NIT of node A. Node A, B, C and D are in the same transmission power level. Node B, C and D are the neighbor nodes of node A and have save in NIT of node A. After node B, C and D execute sleep scheduling algorithm to figure out their Ta and Ts, they would perform Update from neighbor node like action (1) in figure 8. After node A awakens, it would perform Update from local node like action (2)-1 in figure 18. After performing Update from local node, if there are nodes which not update yet, set the active time to 0 and the sleeping time to duty cycle for these nodes like action (2)-2 in figure 10.

Figure 8. Update NIT table of Node A

��	Interrupt point Time (Tirq)

In order to achieve an effective energy distribution through sleep scheduling algorithm, use a parameter known as Interrupt Point Time (Tirq) to conserve more energy. When the node state is active and the wait count is bigger than or equal to 3. After a round is finished and the node has not started transmitting data, an interrupt point time (Tirq) will be triggered. This trigger interrupts the current state of the node and let the node go sleep. Tirq would be set to the current time and the remnant active time would be added to the sleeping time. The interrupt time is calculated as following:

IF (wait count >= 3) AND (status = ‘active’) THEN

Tirq = current time

Update Ts = Ts + (Ta – Tirq)

End

Figure 9 is an example for using interrupt point time (Tirq). Let us assume that the active time (Ta) is set to 6, the sleeping time (Ts) is set to 4 and interrupt point time is set to Ta/2. After three duty cycle timeslots in which no transmissions take place, interrupt time point would be triggered and Tirq would be set to the current time. The node would go sleep and add the remaining Ta time to the Ts time. Consequently, the Tirq effectively puts an active node to sleep to conserve further energy.

Figure 9. Interrupt point Time usage example

��	Transmit Packets and Adjust Power Level

When a node receives a packet, it first determines the strength of the signal against in the NIT table and accordingly adjusts the table information for example if the signal is weaker, it implies that the previous power level needs to be increased to prevent possible transmission failure. Then, it needs to determine that if there is a node can transmit information to the base station. The node must transmit packets to the node which the layer is not bigger to itself. If there is node which can transmit information to the base station, execute data transmission and adjust Ta to let the transmission can be completion properly. If there is no node, keep the current status and wait for the next transmission until the duty cycle is over and enter sleep scheduling algorithm to figure out the Ta and Ts for the next duty cycle. Figure 9 is the detail flow to transmit packets and adjust power level.

Figure 10. Transmit Packets and Adjust Power Level

4	Simulation

4-1	Packet Reception Rate under Sleep Rate

When a sensor node detects the information, it must transfer the information to the base station to let the base station can use the information. If it cannot find the neighbor node to transfer the information, it would be result in the data loss. As shown in Figure 11, there is no mechanism to scatter the sleeping nodes in original sleep scheduling algorithm (SS-old). When the sleep rate is 25%, all the sleeping nodes may be in the transmission route and it results in that the packets loss rate is 25%. Comparatively, the packets reception rate is 75%. Following this, when the sleep rate is 50%, the packets reception rate is 50%. When the sleep rate is 75%, the packets reception rate is 25%. Add a mechanism to adjust the location of the sleeping nodes and prevent all neighbor nodes sleeping together in the improved sleep scheduling algorithm (SS-new). No matter what the sleep rate is, it can guarantee that there is node awake to do transmit and the packets reception rate keeps in 100%.

Figure 11. Packet Reception Rate under Sleep Rate

4-2	Consumption

Two factors must be considered in the power saving research: 1. Consumption; 2. Packets loss rate. Reduce power consumption to extend the network lifetime. But it also needs to consider the packets loss rate. In original sleep scheduling algorithm (SS-old), even though there is low power consumption, it cannot guarantee that there is low packets loss rate concurrently. There is more power consumption in the improved sleep scheduling algorithm (SS-new), but it can guarantee that there is low packets loss rate. Figure 12 is the power consumption which transferring information back to the base station once. When the sleep rate of SS-old is 25%, the power consumption is 75%×(the consumption of packets transmission success)+25%×(the consumption of packets transmission failure). When the sleep rate of SS-new is 25%, the consumption is 75%×(the consumption of packets transmission success under no sleeping nodes adjustment)+25%×(the consumption of packets transmission success under sleeping nodes adjustment). Following this, the consumption under 50% sleep rate and 75% sleep rate can be figured out. As shown in figure 22, SS-new compares with SS-old only increases little consumption.

Figure 12. Consumption

4-2.1	Packet Reception Rate under Rounds

Two factors must be considered in the power saving research: 1. Extend network lifetime; 2. Reduce packets loss rate. These two results are usually adverse. For extending network lifetime, the packets loss rate may be increased. For reducing packets loss rate, the consumption may be increased and the network lifetime would be decreased.

Figure 13 is the relationship between the packets loss rate and the network lifetime. no SS means the wireless sensor networks with out sleep scheduling algorithm. All the sensor nodes are awake for no SS, and it can complete 35 rounds and no packets loss rate. SS-old can complete 43 rounds but have some packets loss rate. SS-new can complete 40 rounds which is between no SS and SS-old and no packets loss rate. SS-new can resolve effectively the problem of the packets loss rate.

Figure 13. Packet Reception Rate under Rounds

5	Conclusions

For WSNs, the design of the sleep scheduling algorithm needs to overcome the problem of the data loss. Because the sensor nodes go sleep, they cannot do data transmission and may cause the data loss.We realize that the improved algorithm proposed by this thesis has resolved the data loss problem of the original algorithm. From the simulation results, SS-new compares with SS-old only increases little consumption. The lifetime of SS-new is shorter than the lifetime of SS-old but it is still longer than the lifetime of no SS. Therefore, SS-new not only resolves the data loss problem but also keeps the low power consumption to effectively extend the network lifetime.

Reference

[1] I. F. Akyildiz, W. Su, Y. Sankarasubramaniam, E. Cayirci, �Wireless sensor networks: a survey,� Computer Networks of Elsevier Journal, Mar. 2002, pp.393-422.

[2] A. Sinha, A. Chandrakasan, �Dynamic Power Management in Wireless Sensor Networks,� IEEE Design and Test of Computers, March-April 2001, Vol. 18, Issue 2, pp. 62-74.

[3] Deborah Estrin, John Heidemann, and Wei Ye, �An Energy-Efficient MAC Protocol for Wireless Sensor Networks,� IEEE INFOCOM 2002, 2002, Vol. 3, pp.1567-1576.

[4] I. Demirkol, C. Ersoy, F. Alagoz, �MAC protocols for wireless sensor networks : a survey,� IEEE Communications Magazine, Apr. 2006, Vol. 44, Issue 4, pp.115–121.

[5] Ying-Hong Wang, Chin-Yung Yu, �A Power Control Mechanism based on Sleep Scheduling for Wireless Sensor Networks,� Ph.D. Thesis Dissertation, University of Tamkang, January 2009.

[6] His-Feng Lu, Yao-Chung Chang, Hsing-Hsien Hu, Jiann-Liang Chen, �Power-Efficient Scheduling Method in Sensor Networks,� 2004 IEEE International Conference, 10-13 Oct. 2004, Vol. 5, pp.4705-4710.

[7] A. Boukerche, X. Cheng, and J. Linus, �Energy-Aware Data-Centric Routing in Microsensor Networks,� Proceedings of the 6th ACM international workshop on Modeling analysis and simulation of wireless and mobile systems, 2003, pp.42-49.

[8] Barbara Hohlt, Lance Doherty, Eric Brewer, �Flexible Power Scheduling for Sensor Networks,� Proceedings of the third international symposium of Information Processing in Sensor Networks (IPSN), 2004, Oral presentation session 3, pp.205-215.

[9] Mihail L. Sichitiu, �Cross-Layer Scheduling for Power Efficiency in Wireless Sensor Networks,� IEEE INFOCOM 2004, 7-11 March 2004, Vol. 3, pp.1740-1750.

[10] J. Chen, S.-H. Gary Chan, Q. Zhang, Wen-Wu Zhu, and J. Chen, �A distributed power adaptation algorithm for multimedia delivery over ad hoc networks,� Proceedings of 2003 International Conference on Multimedia and Expo, July 2003, Vol. 1, pp.I-293-I-296.

[11] V. Kawadia and P. R. Kumar, �Power Control and Clustering in Ad hoc Networks,� IEEE INFOCOM 2003, 30 Mar.-3 Apr. 2003, Vol. 1, pp.459-269.

[12] A. I. El-Osery, D. Baird and S. Bruder, �Transmission power management in ad hoc networks: issues and advantages,� Proceedings of 2005 IEEE Networking, Sensing and Control, Mar. 2005, pp.1043-1048.

[13] P. Floreen, P. Kaski, J. Kohonen, and P. Orponen, �Lifetime maximization for multicasting in energy-constrained wireless networks,� IEEE Journal on Selected Areas in Communications, Jan. 2005, pp.117-126.