Double-Flow Type Solar Air Heaters

The performance of double-flow type solar air heaters, in which air is flowing simultaneously over and under the absorbing plate, is more effective than that of the devices with only one flow channel over or under the absorbing plate because the heat-transfer area in double-flow systems is double. The effect of the fraction of mass flow rate in the upper or in the lower flow channel of a double- flow device on collector efficiencies, has been also investigated theoretically and experimentally. Considerable improvement in collector performance is obtained by employing a double-flow type solar air heater, instead of using a single-flow device, if the mass flow rates in both flow channels are kept the same.