ELECTROPHORESIS OF NANO-POLYELECTROLYTES IN AQUEOUS ELECTROLYTES SOLUTIONS: INFLUENCE OF IONIC POLARIZATION

L.H. Yeha, K.L. Liua, J.P. Hsua and Shiojenn Tsengb

a Department of Chemical Engineering, National Taiwan University, Taiwan

b Department of Mathematics, Tamkang University, Taiwan

topology@mail.tku.edu.tw

The electrophoresis of a polyelectrolyte, an entirely porous, charged nanoparticle, in various types of aqueous electrolyte solution is modeled taking account of the presence of multiple ionic species, and its applicability is verified by the experimental data of succinoglycan in the literature. We show that, in addition to the electroosmotic flow around a polyelectrolyte, two types of competing polarization effect are also significant: counterion polarization and coion polarization, both of them depend largely on the thickness of the double layer. The presence of these two polarization effects yields profound and interesting electrophoretic behaviors that are distinct to polyelectrolytes. The results gathered provide necessary theoretical background for the interpretation of various types of electrophoresis data in practice. Typical examples include that of a nanopore-based sensing device used, for instance, in DNA sequencing.