複合積層板之部分應力有限帶素法分析

Based on the higher-order laminated plates theory, the partial hybrid stress model is combined with the finite strip method to analyze the orthotropic laminated plates in this paper. The through- thickness effect of transverse shear stresses can be properly predicted by the nonlinear displacement field of higher-order plate theory and assumed hybrid model of(.tau./sub xz/, .tau./sub yz/) in the partial hybrid stress model. Several examples are illustrated to validate the accuracy and applicability of present model.