部分應力高階層梁元素之自由振動分析

The partial hybrid laminated beams element is applied to the free vibration analysis of orthotropic laminated beams in this paper. The kenetic energy is added to the modified Jing-Reissener principle. Through vibration, the element stiffness is the assembly of flexural stiffness in displacement version and transverse shear stiffness in hybrid version. The present element obtains accurate results, which approach the exact solution of frequencies based on the refined C/sup 1/ higher-order beam theory. Some important observations are also concluded on the frequency analysis of orthotropic laminated beams.