高階積層板之雙模數有限元素位移法自由振動分析

The free vibration analysis of bimodulus laminated platesis established by using the higher-order plate element in this paper. The inertia effects are considered by adding kinetic energy to the potential energy. Several comparative examples include single-and two-layer bimodulus plates. The natural frequencies and neutral surface locations are determined. The numerical results are compared to the available analytical solutions, and excellent agreement is observed. Apparently, more accurate results than the first-order theory results are obtained herein.