沉陷檢測與地下水位等兩項資料之其他用途

The continual overdraft of the groundwater from a confined saturated acquifer will result in a severe land subsidence. Therefore, in a land subsidence field several observation wells were sunk to obtain two items of the continuous data, the land settlement and the groundwater level, in order to understand the variation of the ground level and to control the pumping of the groundwater. In addition to these purposes, this paper investigates the other purposes for utilizing of the above two mentioned field data in coorporation with a field survey of well, i.e., the indirect determination of the annual variations of the permeability K and compression index Cc of the stratum.