Construction of Cellular IP Networks for Mobile Multimedia Communication Services

Nowadays, wireless communication that provides voice only is notsufficient to support the user's need. Therefore, it's an importantfeature of next generation wireless communication to offer thiscapability through mobile Internet. Mobile IP allows mobile hosts tochange their location and reduce data packet loss probability inwireless communication networks. However, mobile IP still have somedefects in handoff and route aspects. Thus, cellular IP protocol isproposed for routing of lP diagrams to mobile stations and fasthandoff control in a limited geographical area. It can cooperate withmobile IP to provide wide area mobility support. In this paper, weoffer a Soft-handoff method to improve Quality of Service and resourceswitching management to reduce data packet loss for mobile multimediacommunication in cellular IP and mobile IP network.