分離式滑動模式電力系統穩定器

This paper addresses a new approach for sliding mode control to design the power system stabilizers (PSS). The design of a PSS can be formulated as an optimal linear regulator control problem. However , implementing this technique requires the design of estimators. This increases the implementation and reduces the reliability of control system. These reasons, therefore, favor a control scheme that uses only some desired state variables, such as torque angle and speed. To deal with this problem, we use the optimal reduced models to reduce the power system model into two state variables system by each generator and use sliding mode control to find control signal of each generator, moreover, use optimal decentralized stabilizer to achieve control each generator. The advantages of the proposed method are illustrated by numerical simulation of the two machines-infinite-bus power systems.