應用於DVB-T基頻接收機之2K點快速傅立葉轉換器分析及模擬

In this paper, we introduce DVB-T systematic structure and specification, then probe into the advantage and disadvantage of Memory base and Pipeline base two kinds of structure. In order to design conveniently, we decide to design 2048 FFT with DIF Pipeline structure by Radix2/sup 2//2 algorithm. Finally, we simulate 2048 FFT of DVB-T receiver base band on Mat lab, and verify its result.