All in One 315 MHz ASK UHF Receiver

An all in one integrated 315MHz ASK UHF receiver is proposed in this paper. This receiver is a monolithic ultrahigh frequency (UHF) receiver including radio-frequency (RF) front-end, intermediate-frequency (IF) stage, base-band stage and final filter without any spiral inductor. The proposed receiver was implemented with UMC 0.5.mu.m CMOS DPDM processes. The sensitivity of the proposed receiver is -73dBm. Its data rate can be operated at 2.4kbits. The power consumption of this chip is 65mW. The chip size is 1370*1370.mu.m/sup 2/.