PID控制器最佳設計

This work presents a optimal approach to design PID controllers. Theproblem formulation of the design PID controller adopt fourperformance index maximum overshoot, rise time, setting time andintegral absolute error as the objective. Moreover, we propose asolution algorithm based on the simulated annealing technique todetermine the controller parameters for getting a well performance fora given plant. Simulation results demonstrate that better controlperformance can be achieved in comparison with Ziegler-Nichols method.