極音速膨脹與壓縮流動邊界值問題之相似解及其應用

The similarity solutions of hypersonic small disturbance potential equation to the boundary value problem of centered expansion and compression waves are given. In particular, the analytical solutions of the wedge airfoil including oblique and curved shocks at leading and trailing edges are constructed. The lift and drag coefficients of flat plate with angle of attack are also calculated from potential theory and the result agrees well with that obtained from the shock-expansion theory.