視障輔助多功能手杖之設計製造

It is necessary to use cane to walk for the blind and visually impaired person. The used foldable cane has a lot of flaw. And it is unable to be used for a long time. The purpose of this research is to design and produce a multi-functional cane for the blind or visually impaired person. The cane is foldable, less weight, high strength, and fluorescent. It is proved that the structure of the new cane is stronger than the exited one by the finite element method ( FEM ). By the new mechanism of linking, it is able to produce undistorted response when it is knocked, and it is easy to joint and decompose the foldable cane. Finally, some new ideas are attached to the handle of the cane to provide further assistance. The prototype of initial design has been tested by the blind and visually impaired persons. And their opinions were incorporated into the modified design.