移動式起重機過捲預防裝置之安裝可行性改進研究

The purpose of this study is to design and produce an truck cranes over-winding cutout device for the works in Taiwan. For the time being, most of the over-winding cutout or warning devices are imported from forgive countries. The cost is expensive for the users of truck cranes. Some of the safety devices only work as an warning alarm. So, it is still dangerous if the safety device can not cutout the power of the truck carne. In this study, truck crane workers are interviewed first to understand their operating behavior and what they need in the future improvements of safety device in truck cranes. Then the evaluation of all possible improvements available is the next step on the way to redesign a new model of the over-winding cutout device and further the cutout device.