Semi-SOI Pressure Sensors as Lab-on-Chip Systems Applied to Micro Fluid Dynamics

This paper proposed a new framework of micro sensor technology toimplement the lab-on-chip systems used in micro fluid dynamics andbiomedical applications. The semi-SOI pressure sensors fabricated onglass substrates provide a platform for silicon micro channels as wellas silicon micro heat-pipes to be operated and monitored in an in-situway. Platinum thin-film resistor evaporated on glass substrates(#7740) augment the capability of temperature measurement beyond thepressure measurement mentioned above. Package issue of second anodicbonding and the thermal noise due to nearby sensor array are ofprimary concerned at the present stage.