TUUSAT-1A 微衛星姿態控制系統設計與分析

This thesis focuses on the design and analysis of the attitude control system (ACS) and the software simulator TUUSIM (TUUSAT-1A SIMulator) for microsatellite TUUSAT-1A. The subsystem requirements of the TUUSAT-1A ACS are allocated and defined according to the mission objectives and requirements. The passive magnetic attitude control system (PMACS) consisted of 2 permanent magnets and 4 hysteresis rods wrapped with shorted coils was adopted. In order to verify the performance of TUUSAT-1A ACS, the software simulator was developed by the MATLAB computer language. In order to achieve more realistic simulation and performance analysis, the full-software analytical tool TUUSIM was developed by the Mechanical Subsystem Research Team. TUUSIM is a mission simulator developed on the basis of orbital propagator and attitude simulator, and integrated the codes of thermal distribution, communication coverage, power generation, and mode operation together.