TUU SAT-1微衛星結構設計分析

This paper provides a completed design method of structure subsystemof microsatellite TUU SAT-1 which was accomplished the primary designto arrange the payload subsystems. The uncertain parts of payloadsubsystems are designed by referring to developed microsatellites inthe world. The required specification of ejection system is the HESejection system of NASA. The finite elemental software I- DEAS MS6 isused to accomplish the structure model of satellite and connectioninterface. The stress and the nature frequency of satellite'sstructure subsystem are analysis and satisfied the missionrequirements of TUU SAT-1.