迷你平板迴路式熱管之研製

IC industry is one of Taiwan industries gaining strong global competitiveness. With increasing functions of electrical manufactures, we need advanced cooling systems to solve the high temperature problems resulted from interior concentrative power consumption of electric device. The available fan-heat sink mechanism will be certainly not satisfying with the cooling requirement of prospective electric devices. So we bring up the study of Flat Plate Loop Heat Pipe (FPLHP) utilizing the phase change phenomenon to enhance cooling ability. In this study, FPLHP consisting of an evaporator, vapor line, air condenser, and liquid line was fabricated and characterized. Evaporator with comb grooves and copper mesh is a novel design to increase capillary pumping capacity. FPLHP were realized by bonding a glass onto copper substrate, resulting in a transparent cover for observation. Methanol, Water, and Freon (HCFC 141b) were used as the working fluid in the experiment. Preliminary result showed that FPLHP filled with methanol could dissipate heat more than 68W. Under air cooling the total thermal resistance of such a system is 1.3 .degree./W and depends strongly on the cooling conditions and the radiator efficiency. Research work is continuing for the heat transfer limitation, different fluid charge rate and optimization of the FPLHP size design in an effort to improve the cooling performance of the notebook computer.