迴流效應對行程平板型質量交換系統之質傳效率研究

A study on improvement in performance of multi-pass parallel-platemass exchangers with uniform wall concentration and with externalrefluxes has been investigated by use of an orthogonal expansiontechnique. Comparisons of analytical results are made with single-passoperations of the same size (Without sheets inserted and withoutrecycle). Considerable improvement in the mass transfer efficiency forlarge mass Graetz numbers is obtainable by introducing therecycle-effect concept in designing such multi-pass operations. Theeffect of sheet location on the enhancement of mass transferefficiency as well as on the increment of power consumption, has beendiscussed.