Site Survey Estimation Method for Wireless Ad Hoc Networks

The thickness and angle of obstacles have been considered by the site survey estimation method for the wireless ad hoc network with the path loss contour estimation method and the system performance measurement. The site survey estimation tool can be realized by the AutoCAD and Linear Prediction Estimation (LPE) method. This tool is very important for the future use of the commercial wireless LAN systems for field tests and cell planing of Ad Hoc network.