ERMES/FLEX呼叫器中頻積分三角頻率數位轉換調變鑑頻電路之研究

In this paper, we design the IF frequency discriminator for the ERMES/FLEX pager system with the technology of the delta-sigma modulator. This circuit can discriminate the 2/4 level FSK with the digital demodulation method. In this paper, we use the VHDL(Very High Speed Integrated Circuit Hardware Description language) to simulate this circuit. We also do some experimental results to verify the function of the delta-sigma frequency discriminator with the ALTERA chip.